## Slide 2
Prerequisite : 8086 Microprocessor and Process Memory Map

## Slide 3
Powering Up : Reset
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
Physical address =(CS<<4) + IP
=0xFFFF0
First Instruction fetched from location 0xFFFF0
Processor in real mode
Limited to 1 MB addresses
No protection; no privilege levels
Direct access to all memory
No multi-tasking
First instruction is at right on top of accessible memory
should jump to another location
0x100000
0xFFFF0
0xF0000
0
BIOS
First instruction
Inaccessible memory (RAM)

## Slide 4
Powering Up : Reset
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
Present in a small chip connected to the processor
- FLASH/EPROM
Does the following
Power on self test
Initialize video card and other devices
Display BIOS screen
Perform brief memory test
Set DRAM memory parameters
Configure plug & play devices
Assign resources (DMA channels & IRQs)
Identify the boot device
Read sector 0 from boot device into memory location 0x7c00
jump to 0x7c00
BIOS

## Slide 5
Powering Up : Reset
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
Sector 0 in the disk called Master Boot Record (MBR)
Contains code that boots the OS or another boot loader
Copied from disk to RAM (@0x7c00) by BIOS and then begins to execute
Size 512 bytes
  446 bytes bootable code
  64 bytes disk partition information (16 per)
  2 bytes signature (0xAA55)
BIOS
MBR Execution
Typically, MBR code looks through partition table and loads the bootloader (such as Linux or Windows )
Or it may directly load the OS

## Slide 6
Powering Up : Reset
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
BIOS
MBR Execution
N sector disk drive. Each sector has 512 bytes
Sector 0 MBR
Sector 2
Sector 3
Sector N-1
Sector 1
Code (440 bytes)
DS (4 bytes)
Null (4 bytes)
Partition table( 64 bytes 16 bytes for each
Signature (2 bytes)

## Slide 7
Powering Up : Reset
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
BIOS
MBR Execution
The bootloader may be present in the MBR (sector 0) itself
Bootloader
Loads the operating system
May also allow the user to select which OS to load in case dual boot
Other Jobs done
Disable interrupt
Setup GDT
Switch from real mode to protected mode
Read operating system from disk

## Slide 8
Booting Linux
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
BIOS
MBR Execution
Bootloader (GRUB)
Three stage of grub
stage 1 : 446 bytes boot.img
stage 1.5: core.img
stage 2 : load kernel

## Slide 9
Booting Linux
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
BIOS
MBR Execution
Bootloader (GRUB)
Kernel is loaded into memory
Kernel initiates itself needs to mount the root(/)file system
Kernel Initialization
How the Linux Kernel access the LKM for mounting the root (/) file system, which are present on the root file system itself?
/boot/initrd.img uncompressed and loaded
Content of initrd file serve as temporary root file system
Kernel executes pivot_root command
Kernel initialize schedular PID = 0
Fork and execute /sbin/init
/lib/system/systemd
/bin/systemd

## Slide 10
Booting Linux
Powering on Reset
Every register initialized to 0 except
CS=0xF00, IP=0xFFF0
BIOS
MBR Execution
Bootloader (GRUB)
Kernel Initialization
The system vs init :
Older Linux distro( Ubuntu14, Debian6, RHEL6, CentOS6)
Newer Linux distro (Ubuntu15.04, Debian7, RHEL7, CentOS7)
Fast Booting
Init (run-level) system (targets)
0: poweroff poweroff.target
1: rescue rescue.target
2: multi-user(w/o nw) multi-user.target
3: multi-user(nw) multi-user.target
4: unused
5: graphical graphical.target
6: reboot reboot.target

## Slide 11
Bonus

## Slide 12
Multiprocessor Booting
One processor designated as ‘Boot Processor’ (BSP)
designation done by either Hardware or BIOS
All other processors are designated AP (Application Processors)
BIOS boots the BSP
BSP learns system configuration
BSP triggers boot of other AP
Done by sending an Startup IPI (inter processor interrupt) signal to the AP